## Slide 1: Bathtubs, Slinkies, and Mirrors
Using common experiences
to visualize wave physics in antenna feed line systems
Clallam County Amateur Radio Club Bill Peterson – K7WWP October 10 , 2018

## Slide 2: New ideas that you already know
It’s easier to learn and understand something when the new idea fits into your vision of reality like a piece into a jigsaw puzzle.
It’s just an extension of what you already know.
Once you know how it fits, it’s easier to understand and remember.
My goal is to make wave physics on antenna feed systems easier to understand.
Notes: This is how high-school and most college classes were for me.
Until I got halfway through my junior year, then suddenly things were hard as I was getting into the realm of things that weren’t intuitive.
Tonight, I hope we can explore some intuitive commonly observable phenomena that helps us understand antenna transmission line systems.

## Slide 3: A wave travels in some medium
A sound wave in the air
A wave in water
A wave down a string
A wave of light
A wave of electricity down a wire

## Slide 4: And Then the wave Hits Something
A sound wave in the air
    The end of the air (the canyon wall)
A wave in water
    The end of the bathtub
A wave down a spring
    The end of the spring
A wave of light in the air
    A window or mirror (The end of the air)
A wave of electricity down a wire
    The end of the wire

## Slide 5: A sound wave
Echo
  Echo
    Echo
      Echo
        Echo
          Echo
            Echo

## Slide 6: Spring Demo

## Slide 7: Spring Demo
Notes: See the Wave.
See the Wave reflected back.
-- Ask for volunteer to hold end of spring.
-- See the wave reflected back even if the end is secured.

## Slide 8: A ray (Wave) of Light hitting a mirror

## Slide 9: The end of the wire
We can’t see anything
But in all other cases, the wave bounced back
Won’t that also happen with electricity at the end of the wire?
  Power spikes
    Clicks you hear on the radio when you flip a light switch
    Power spikes that cause sever overvoltage and destroy electronics
      The inductive nature of power loads makes this problem far worse
      Surge protectors
Notes: Power spikes are also caused by abrupt changes in voltage over reactive loads.

## Slide 10: Standing Waves
Waves move in one direction
Waves reflect back
The combined effect is standing waves

## Slide 11: Standing waves off the side a bridge

## Slide 12: Standing Waves and resonance
When the reflected wave is reflected back
And it matches and reinforces the original wave
Then it builds up, finally limited by the resistance in the system.

## Slide 13: Demo Standing Waves ON SPRING

## Slide 14: Examples of Resonant waves
Vibrating stings on a musical instrument such as a guitar, piano, violin
Column of air in flute or trumpet
Light in a laser
Radio waves in a microwave oven

## Slide 15: Will Standing Waves hurt my Radio?

## Slide 16: Will Standing Waves hurt my Radio?
Let’s look at what standing waves will do to a bridge

## Slide 19: Standing waves in a microwave
Microwave and peeps.
  2.45 G
  300 / 2450 = .1225 meters
  ½ wavelength = .061 meters
  ½ wavelength = 2.4 inches
The rotating plate moves the food so the standing don’t heat just parts of the food.

## Slide 20: Partially melt peeps in microwave without the rotating plate.

## Slide 21: Open/Short
Spring Demo

## Slide 22: Back to the Spring
Reflections with free end
Momentum
Reflections with secured end
Energy

## Slide 23: Mismatches cause reflection
Shorts cause reflection in one direction
Opens cause reflections in the other direction
As you move between a short and an open
  The reflection will get smaller, minimize, and get larger in the opposite direction
  At the minimized point, you have the best match.
Discontinuities in the feed line
  Kinks
  Wrong connectors
  Bad connection

## Slide 24: Mismatch high impedance to Low Impedance

## Slide 25: Mismatch Low impedance to High impedance

## Slide 26: Partial reflections

## Slide 27: Partial reflection of waves of light

## Slide 28: Somewhere in the middle
Between the wave that is reflected positively
And the wave that is reflected negatively
Is a point where no wave is reflected at all. This is a matched junction.
Reflected waves travel more than once on the feed line.

## Slide 29: Match / Mismatch demo

## Slide 30: Transmission Line Losses
Refection Points
  Mismatched Feedline / Antenna
  Mismatched sections of Feedline
  Kinks and feed-line damage
  Mismatches because connector is not rated for higher Frequency
    Ex. 239 connectors on UHF

## Slide 31: Finally we talk about antennas

## Slide 32: Antenna Tuner in Shack

## Slide 33: Antenna Tuner at Antenna Feed Point

## Slide 34: Ladder Line is great

## Slide 35: Line Losses on 100 feet of feed line
Feed Line | Freq | SWR 1:1 | Loss | SWR 3:1 | Loss | SWR 10:1 | Loss
RG-58 Coax | 10 MHz | 1.12 dB | 23 % | 1.66 dB | 32 % | 3.71 dB | 67%
RG-213 Coax | 10 MHz | 0.62 dB | 13% | 0.97 dB | 20% | 2.40 db | 42%
450 ohm Ladder | 10 MHz | 0.21 dB | 5 % | 0.33 dB | 7.4% | 0.93 dB | 19%

## Slide 36: Open / Short Revisited
Short reflect in opposite direction
Opens reflect in same direction
Short (Fixed end) spring stretches out, and is then pulled back, but because the end is fixed, the pull back is against the wave. The reflection is reversed.
Voltage is zero
Current flows
Open spring swings, then swings back. Reflection is same.
Voltage swings freely
Current is zero

## Slide 37: Quarter Waves
Open on one end appears Closed (Shorted) on the other
Notes: Only half of you have their eyes glazed over. Let’ see if I can get the rest of you.

## Slide 38: Quarter Wave Stub

## Slide 39: Quarter Wave Stub Filter
At a specific frequency:
Open quarter wave stub will appear as a short.
Can be used to short out harmonics. Use open quarter wave stub at harmonic frequency.
My transmitter at 40 meters with second harmonics (20 meters)
  Open quarter 20 meter stub will short out my 2nd harmonics.

## Slide 40: Quarter Wave Transformers

## Slide 41: Quarter Wave Transformers

## Slide 42
An infinite number of reflections and re-reflections sum up
  No reflections
  No power loss
  Load appears as Z0

## Slide 43
Z0
ZT
ZL
If Z of the load is high,
the other end of a quarter wave section makes it look low. ZT combined with the inverted ZL = Z0
Z0
ZT
+ZL inverted
Looks like Z0

## Slide 44: Quarter wave transformers on PC Boards

## Slide 45: Microwave - Stepped Guide - Variable guide (Microwave horn)

## Slide 46: These are all forms of matching from sound generator to the open air

## Slide 47: Quarter Wave anti-reflective coating

## Slide 49: In Summary, waves are waves